## Slide 1
Calculating the Throughput Ceiling and Its Interactivity Cost
An illustrative capacity model for SGLang serving
Kimi K2.5 · ISL 8K / OSL 1K · TP=4 B200 + FlashInfer TRT-LLM vs. MI355X + AITER
Capacity is a frontier: maximize throughput subject to TTFT and ITL SLOs.
Kimi K2.5 · ISL 8K / OSL 1K · TP=4
1

## Slide 2
Executive summary
MEMORY BOUND
Resident batch
KV capacity determines how many long-context requests can remain active.
COMPUTE BOUND
Kernel saturation
Backend kernels determine when additional batching stops improving tokens/s.
SLO BOUND
Interactivity
Larger batches increase decode-step time and therefore ITL.
The key relationship
Output throughput ≈ Resident decode batch ÷ Decode-step time
Throughput may rise while ITL worsens—both observations can be true.
Kimi K2.5 · ISL 8K / OSL 1K · TP=4
2

## Slide 3
Workload anatomy
Why “total throughput” can mislead
9,216 tokens / request
ISL 8,192 OSL 1,024
Input / prefill 89%
11%
TOTAL TOKEN THROUGHPUT
(Input + output) / time
Mostly measures prefill scaling for this 8:1 workload mix.
GENERATION THROUGHPUT
Output tokens / time
The better metric for decode capacity and ITL trade-offs.
Report input TPS, output TPS, total TPS, TTFT, and ITL separately.
Kimi K2.5 · ISL 8K / OSL 1K · TP=4
3

## Slide 4
Step 1 — Bound the resident batch
Offered concurrency
Client-side request pressure
Request slots
Auto max_running_requests
KV capacity
max_total_num_tokens ÷ live tokens/request
Resident decode batch
Requests actually advancing on GPU
Bresident ≤ min(BKV, request slots) · Offered concurrency may be much larger
Kimi K2.5 · ISL 8K / OSL 1K · TP=4
4

## Slide 5
Step 2 — Calculate KV capacity
Kimi K2.5 MLA with FP8 KV
Per-token KV geometry
61 layers × (512 latent + 64 RoPE) × 1 byte FP8
= 35,136 bytes / token / GPU
TP=4 does not divide the compressed MLA KV token cost on each rank.
Per-request KV cost
35,136 bytes × (8,192 + g)
After prefill: 274.5 MiB
At 1K output: 308.8 MiB
BKV,end = floor(TKV / 9,216)
Kimi K2.5 · ISL 8K / OSL 1K · TP=4
5

## Slide 6
Step 3 — Compare raw memory headroom
Illustrative upper bounds before runtime reservations
B200 · NVIDIA Kimi-K2.5-NVFP4
MI355X · AMD Kimi-K2.5-MXFP4
180 GiB HBM
137.6 GiB weights
Raw headroom 42.4 GiB
288 GiB HBM
130.2 GiB weights
Raw headroom 157.8 GiB
Raw 9K KV bound
B200 ≈ 141
MI355X ≈ 523
Use /server_info max_total_num_tokens for the real bound; allocator, graph, VLM, and backend reserves reduce these raw values.
Kimi K2.5 · ISL 8K / OSL 1K · TP=4
6

## Slide 7
Step 4 — Translate batch size into throughput and ITL
Output TPS(B) ≈ B / t(B)
ITL(B) ≈ t(B)
If batch grows faster than step time: • throughput increases • ITL also increases
Illustrative normalized example
128
256
512
1024
Offered concurrency →
TPS ↑
More throughput but longer decode steps
Kimi K2.5 · ISL 8K / OSL 1K · TP=4
7

## Slide 8
Why B200 shows a ceiling while MI355X keeps scaling
1 · MEMORY
~3.7× raw KV headroom
MI355X can sustain a much larger resident long-context batch.
2 · KERNELS
Different saturation points
FlashInfer TRT-LLM reaches useful occupancy earlier; AITER persistent MLA can benefit from larger batches.
3 · METRIC MIX
Prefill dominates total TPS
At 8K/1K, improved AITER prefill batching can raise total TPS while ITL deteriorates.
B200 pattern
Capacity / compute knee near ~128 → total TPS flattens
MI355X pattern
Resident batch scales into the hundreds; at 1024 offered concurrency, queueing and prefill batching may still raise total TPS.
Kimi K2.5 · ISL 8K / OSL 1K · TP=4
8

## Slide 9
Step 5 — Bound end-to-end throughput
No prefill/decode overlap
QPS ≤ 1 / (ISL / P + OSL / D)
Total TPS ≤ 9,216 × QPS
Ideal independent overlap
QPS ≤ min(P / ISL, D / OSL)
Real mixed scheduling lies between the bounds
Queue
Prefill · P
Decode · D
Done
P and D should be measured at steady state; a hardware-only roofline is rarely predictive for distributed MoE serving.
Kimi K2.5 · ISL 8K / OSL 1K · TP=4
9

## Slide 10
Measure the bound instead of guessing it
Live SGLang signals
num_running_reqs
Actual resident scheduler batch
num_waiting_reqs
Offered load beyond admission
token_usage
KV pressure
gen_throughput
Decode—not total—throughput
cache_hit_rate
Shared-prefix correction
queues.retracted
KV churn and likely ITL spikes
Query during the sweep
curl -s \ 'http://host:30000/ v1/loads? include=core,queues' | jq
Capture p50 and p99—not only averages.
Kimi K2.5 · ISL 8K / OSL 1K · TP=4
10

## Slide 11
Choose the SLO knee—not maximum concurrency
SLO knee
Concurrency / ITL cost →
TPS ↑
Optimization objective
Maximize output TPS
subject to
p99 ITL ≤ SLO p99 TTFT ≤ SLO
Capacity is workload-specific.
Kimi K2.5 · ISL 8K / OSL 1K · TP=4
11

## Slide 12
Takeaways
1
Separate the limits
Request slots, KV capacity, kernel saturation, and SLOs are different constraints.
2
Use the right metric
At ISL 8K / OSL 1K, total TPS mostly measures prefill; use output TPS for decode.
3
Explain the platform gap
MI355X has far more KV headroom and AITER scales to larger batches; B200 reaches its knee earlier.
4
Optimize for interactivity
Choose the highest output throughput that satisfies p99 TTFT and ITL.
Kimi K2.5 · ISL 8K / OSL 1K · TP=4
12